## Slide 1
Modern Intelligent Hand Prostheses
Tobias Stocker (Advisor: Pascal Weiner)
Seminar: Humanoid Robotics, WS 2017/18

## Slide 2: The Task
Research of recent developments in intelligent hand prostheses
in the last 2-3 years
Overview of important properties
  Design / structure
  Kinematic / dynamic characteristics
  Sensor feedback / embedded systems
Comparison of different prostheses
  What do they have in common?
  What are special features of different hands?
  Do they provide intelligent functions?

## Slide 3: My work so far
Searching for papers with prosthetic hands
Summarizing the important information for each hand
Creating a table with important properties

## Slide 4: Example: SSSA-MyHand and Tact
Name | Developer | Year | Mass | Size | DoFs | Actuators
MyHand | SSSA | 2016 | 478 g | 200x84x56 mm | 4 | 3
Tact | Slide et al. | 2015 | 350 g | 200x98x27 mm | 6 | 6
Name | Integrated Actuators | Transmission System | Sensors | Finger Force | Joint Speed
MyHand | Yes | Geneva drive | Position / Force | 12-31 N | 160-250 °/s
Tact | Yes | Tendons |  | 4.21 N | 249.8 °/s
Name | Number of Fingers | Number of joints | Joints per finger | Actuator type
MyHand | 5 | 10 | 2/2 | Brushless DC Motor
Tact | 5 | 11 | 3/2 | DC Motor

## Slide 5: The next steps
Overview of important properties
  Design / structure
  Kinematic / dynamic characteristics
  Sensor feedback / embedded systems
Comparison of different prostheses
  What do they have in common?
  What are special features of different hands?
  Do they provide intelligent functions?